## Slide 1: A Ball Goes to School – Our Experiences from a CPS Design Experiment
Steffen Peter,
Frank Vahid,
Daniel Gajski,
Tony Givargis
supported by the National Science Foundation

## Slide 2: Outline
Motivation
The Falling Ball Example
Execution
Results

## Slide 3: Motivation
Program to teach CPS design to graduate students
  Typical design flows for CPS design
  Importance of models and their limitations
  Introduction to state-of-the art simulation and modeling tools
Apply small examples that are:
  Easy to understand
  Possible to design and evaluate using a variety of tools and methodologies
  are implementable in the lab

## Slide 4: The Falling Ball Example
Easily understood
Need for precise timing
Physical process needing mathematical modeling
No perfect precision in cyber part
Can be build in the lab

## Slide 5: Execution
Students modeled or implemented the system applying a range of tools (one per student)
Progress, advantages and problems of the selected tools are discussed in the group
Real Implementation
  Raspberry Pie Board, gcc environment
Model based
  Modelica
  Simulink
  Ptolemy
  SystemC

## Slide 6: Simulink / Matlab

## Slide 7: SystemC
//======================================================
// Name : ball.cpp
//======================================================
#include <iostream>
#include "ball.h"
Ball::Ball(sc_module_name name): sc_module(name) {
time_us = 0;
g_force = 0.0000000098;
SC_METHOD(position_update);
dont_initialize();
sensitive << clk.pos();
}
void Ball::position_update() {
position = 0.5 * g_force * time_us * time_us;
//cout << "position:" << position << endl;
//cout << "time: " << sc_time_stamp() << endl;
time_us++;
}
Ball Module
Controller Module
position
physical_clk @1MHz
cyber_clk @ 1KHz
sensor_1
sensor_2
gripper
position = 0
position = 0.5 x a x t2

## Slide 8: Modelica
Height [m]
Time [s]

## Slide 9: Discovered and discussed challenges:
Math and modeling the physical system
Separation of physical and cyber part
Design methodologies of graphical design tools
Selection of an appropriate Model of Computation
Zeno behavior and simulation time resolution issues

## Slide 10: Conclusions
The Falling Ball example is a suitable use case to teach CPS design
Simplicity of the example allows students to focus on the actual CPS design challenges
In four weeks (10h/week) students learned
  how to use CPS design tools,
  model a CPS system,
  run simulations,
  test the system and evaluate the results
Discovered design challenges are good support for lecture

## Slide 11: Thank you