## Slide 1: Tool-Supported Methodology for Component-based Design of Wireless Sensor Network Applications
Steffen Peter and Peter Langendörfer

## Slide 2: Outline
Motivation
Methodology
Model-based assessment
Evaluation and first results
Conclusions

## Slide 3: Wireless Sensor Networks
Large networks of autonomous sensor nodes
Wireless ad-hoc networks
Cooperative monitoring of distributed phenomenon
Notes: Application domains: agriculture, industrial monitoring, critcial infrastructures

## Slide 4: Motivation
WSNs are inherently task-specific
  functions similar, but differ in QoS aspects
No one-fits-all solution
Many individual solutions exist to cope with the challenges of WSNs
  Limited energy, low computation power, small memory
  Demanding ad-hoc radio communication and security challenges
Solutions mostly no add-ons
  Mechanisms influence many layers
Complex trade-offs
  Even complicated for experts
Notes:   Impossible for domain experts (biologists, geologists, engineers)

## Slide 5: Personal Motivation
Sec. random generator
Sec. localization
RSA
DES
TEA
Sec. routing_2
Sec. MAC_2
Sec. robust data storage
Resilient data aggregation alg_1
Resilient data aggregation alg_2
CDA_alg1
CDA_alg2
CDA_alg3
AES
ECC
Sec. routing_1
Sec. MAC_1
AES
ECC
Sec. rout_1
Sec. MAC_1
Sensor node HW
OS
Resilient data aggregation alg_1
CDA_alg2
Sec. robust data storage
Secure local.
Tailor made architecture
Application
Application Requirements
Configuration and Management
Req. vs features of modules
Interoperability of modules
Properties of combination
Building Block

## Slide 6: State of the Art – composition of protocols
KMS [AR06]:
  Selection of Key Management Systems based on user preferences (property must, should, must not)
Cionca [NCB10]
  Proposing protocols based on understandable requirements
  Meta-information in data base of components allows filtering
[AR06] C. Alcaraz and R. Roman. Applying key infrastructures for sensor networks in CIP/CIIP scenarios. In Critical Information Infrastructures Security, volume 4347 of Lecture Notes in Computer Science, 2006.
[NCB10] T. Newe, V. Cionca, and D. Boyle. Security for Wireless Sensor Networks–Configuration Aid. Advances in Wireless Sensors and Sensor Networks, 2010.
Random Pairwise Key
+ sec, sca
- mem, res
Random Pairwise Key
+ sec, sca
- mem, res
Random Pairwise Key
+ sec, sca
- mem, res
Notes: Handcrafting, parametrized middlewares

## Slide 8: Intended design process for WSNs

## Slide 9: Roles in the development process
Requirements
Composition
Deployment
User
End user
Application designer
Network integrator
Req. Repository
Components
Component Developer
Framework Designer

## Slide 10: Roles in the development process
User
End user
Application designer
Network integrator
Component Developer
Framework Designer
Notes: Vision that composition is automatically

## Slide 11: Methodology
Does the system under development satisfies the requirements?
Requirements
components
SYSTEM
Models
How to define requirements?
understood by users
Precise for the system
Formal framework
Find models to express properties as function between requirements and system
Component and system model

## Slide 12: Requirements
Requirements
User
Requirements
Technical
Requirements
Requirements are:
  Technical parameters and constraints
  Description of environment
  Description of participants (user, attacker) in the scenario
User requirements are often fuzzy and non-technical
Need for translation of user requirements to technical requirements
  User selects and parameterizes properties from a requirement catalogue
  They will be translated to technical requirements
Example:
Attacker model and capabilities
- Application type (health care, home, industrial)
Required security attributes (concealment, integrity, robustness)
Parameters
Notes: Alternatives: textual, dialog based -

## Slide 13: Methodology: Composition Process
Requirements Catalog
Property Repository
Component Repository
Requirements
Working Model
Composition
init
Input für Selection
Selection
Look for suitable Components
Goal: No conflicts
Notes: Kriterien: Vollständig, Abgeschlossen, Realisierbar Komposition

## Slide 14: Example
INA (In-network aggregation)
security= good
Selection CaMyTs
Selection AES
INA
=1
!= 0
Sec
=good
>= good
CaMyTs
INA :=1
Cipher
=1
!= 0
Sec:= ciph.sec
AES
Cipher :=1
Requirements
Components
Working Model
Sec:=good
Ciph.sec
=good

## Slide 15
MODELS

## Slide 16: General Model Architecture
Energy
Range
Security

## Slide 17: Security Example: Attack Tree Model
System security
concealment
integrity
Read data
Physically (node)
Eavesdrop (radio)
Access to node
Read physically
Read Radio
Decipher packet
Possibility of attacks on
Actual Attacks
Yes/Not

## Slide 18: Example: Attack Tree Model
System security
concealment
integrity
Read data
Physically (node)
Eavesdrop (radio)
Access to node
Read physically
Read Radio
Decipher packet
Requirements
User
Requirements
Technical
Requirements
Possibility of attacks on
components
Composition
System
App: In-house monitoring
Protected nodes,
Outside attacker
AES
SATISFIED

## Slide 19: Example: Attack Tree Model
System security
concealment
integrity
Read data
Physically (node)
Eavesdrop (radio)
Access to node
Read physically
Read Radio
Decipher packet
Requirements
User
Requirements
Technical
Requirements
Possibility of attacks on
App: Water pipeline
Exposed nodes,
Powerful attacker
NOT SATISFIED
components
Composition
System
AES

## Slide 20: Example: Attack Tree Model
System security
concealment
integrity
Read data
Physically (node)
Eavesdrop (radio)
Access to node
Read physically
Read Radio
Decipher packet
Requirements
User
Requirements
Technical
Requirements
Possibility of attacks on
App: Water pipeline
Exposed nodes,
Powerful attacker
SATISFIED!
components
Composition
System
TAMPRES
AES

## Slide 21: Automatic Selection Algorithm
Idea: If it is possible to tell that a system is valid, a program can look for suitable configurations automatically
Backtracking search algorithm was successfully implemented and tested
Theoretical worst case is still NP complete
In practice, typically it is better than brute force because:
  Conflicting components are removed from the design space
  Previous decisions can be remembered
Alternative solution is reasoning as part of the requirement refinement
  radio + robustness  Bluetooth radio,
  or high security  AES
   Often not best solution, restrains less prominent protocols

## Slide 22
EVALUATION

## Slide 23: Evaluation
Implemented tools
For the Component Developer:
  Tool to enter component information
For the Framework Designer:
  Tool to manage models and requirement catalog
For the User:
    Front end to define application requirements

## Slide 24: Setup of Repository
structural view
dependency graph
selection of sub-components
Setting of parameters, dependencies, requirements
Re-usable XML,
part of repository

## Slide 25: Component Selection Tool
Selection of hardware
Selection of required functions
Definition of security properties
Proposed software configuration
Including prediction of footprint
Each change of inputs immediately updates the result
 Fast and easy refinement process
Notes: Tests
  Synthetic tests
  Reproduce results of related work
  Manage complex trade-offs

## Slide 26
Conclusions

## Slide 27: Conclusions
Design process for WSNs
  Catalog-based requirement engineering
  Automatic component selection and composition process
  Based on models that assess system in context of requirements
Feasibility shown in prototypical implementation
Approach can bridge high-level user requirements and low-level technical implementations
  Value for both users and component developers
Notes: Value for Users: Reduces development time and usability of WSNs
Value for Component developers: Improved dissemination

## Slide 28: Thank You
Steffen Peter
peter@ihp-microelectronics.com