## Slide 1: Sens4U: Wireless Sensor Network Applications for Environment Monitoring Made Easy
Krzysztof Piotrowski and Steffen Peter

## Slide 2: Agenda
Background
Use case
Extended module concept
Application logic definition
Ideal configuration
Conclusions

## Slide 3: Scenario 1: Monitoring Beaver Behavior

## Slide 4: Scenario 2: Opencast mine

## Slide 5: Background
Two complementary PhD theses
  ConfigKit – automatic creation of module-based WSN software configurations based on security requirements
  tinyDSM – configurable data storage for WSNs with event detection and user-defined data items, replication and consistency
Combination of these supports accelerated application development
Extensions in both areas needed
  Extension of the ConfigKit concept to software and hardware and arbitrary (not security only) set of requirements
  Simplification of methods allowing the description of application logic that becomes the top-level software module
Environment monitoring applications as the area of the Sens4U project

## Slide 6: Use case
Customer defines her requirements:
  Locations, Measurements, Maintenance, Reliability
The integrator inputs these into the Planning tool
The Expert System combines chosen modules according to the requirements
The Verification process may trigger additional loop, e.g., updating the module pool or adjusting the requirements
The chosen configuration is implemented
We focus on environment monitoring scenarious

## Slide 7: Y-chart analogy
Module Pool

## Slide 8: Roles in the development process
User
End user
Application designer
Integrator
Component Developer
Framework Designer
Module Pool
Notes: Vision that composition is automatically

## Slide 9: Extended module concept
Modules are pieces of software or hardware
  Implement a given functionality or a set of functionalities
The way a functionality is provided is defined by an interface
  Abstract description on functional, object or hardware level
Interfaces define the properties for the provided functionality
  Each module defines values for these parameters
  For both used and provided interfaces
  These properties drive the module choosing mechanism
Modules are stored in the Module Pool
  Developers provide the implementations and descriptions

## Slide 10: Module Pool relations
includes defines that a module belongs to a larger module, e.g., a µC belongs to a node platform.
uses defines the interfaces used by a given module
provides defines interfaces provided by a given module
has_parameter defines the value of a parameter from a provided interface for the given module
requires_parameter defines the required value(s) of a parameter from an used interface for the given module

## Slide 11: Application logic definition
Transformation of the non-technical requirements into a set of technical requirements
The most tricky part of the system

## Slide 12: Requirements
Requirements
User
Requirements
Technical
Requirements
Requirements are:
  Technical parameters and constraints
  Description of environment
  Description of participants (user, attacker) in the scenario
User requirements are often fuzzy and non-technical
Need for translation of user requirements to technical requirements
  User selects and parameterizes properties from a requirement catalogue
  They will be translated to technical requirements
Example:
Attacker model and capabilities
- Application type (health care, home, industrial)
Required security attributes (concealment, integrity, robustness)
Parameters
Notes: Alternatives: textual, dialog based -

## Slide 13: Application logic definition, cont
Possible on different detail/experience levels
  Macroprogramming
  Scripting
  Pure module programming
We identified the most common patterns (requirements catalogue)
  With the focus on environment monitoring
We provide a GUI to define the application logic (Planning Tool) by:
  Providing the ground view for the monitored area
  Defining communication environment and obstacles
  Defining the measuring points, procedures and data dependencies
  Prototype implementation will be available soon

## Slide 14: Methodology
Does the system under development satisfies the requirements?
Requirements
components
SYSTEM
Models
How to define requirements?
understood by users
Precise for the system
Formal framework
Find models to express properties as function between requirements and system
Component and system model

## Slide 15: Methodology: Composition Process
Requirements Catalog
Property Repository
Component Repository
Requirements
Working Model
Composition
init
Input für Selection
Selection
Look for suitable Components
Goal: No conflicts
Notes: Kriterien: Vollständig, Abgeschlossen, Realisierbar Komposition

## Slide 16: The ideal configuration
The configurations that are generated with the tools they influence
Notes: The management tool has to know the node software and hardware. Same for deployment tool that is used to verify the communication links during the deployment. The simulation tool is used to simulate the complete system.

## Slide 17: The ideal configuration
Each configuration consists of modules connected via interfaces
For example:
Interface A
- Parameter A1
- Parameter A2
Interface B
- Parameter B1
Interface C
- Parameter C1
Notes: Modules are connected according to the values of the parameters for the given interfaces. The complete configuration reflects the multilevel choice problem.

## Slide 18: Conclusions
We propose a system that:
supports the non-WSN-experts in the specification of they real-life target system requirements,
provides a module description framework to support computer aided application development and module testing,
allows creating application specific/optimized software and hardware configurations,
does not only suggest software compositions, but also suggests hardware components with diverse granularity (platform, chip, module) and functionality (accelerators, sensors, actuators) to fulfill the given task,
utilizes an user and process model that emphasizes the applicability by non-WSN-experts.

## Slide 19
Thank you for your attention!

## Slide 20: The deployment tool